## Slide 1: Robotic Navigation and Exploration
Final Project
Min-Chun Hu
CS, NTHU
anitahu@cs.nthu.edu.tw

## Slide 2: Basic-Automatic tracking schematic map
You should let your jetbot follow the line in the demo.
START
END

## Slide 3: Advance – Parking schematic map
Try to park on the end sign as near as you can.
end
Perfect line
Basic
line
end

## Slide 4: Advance – Avoidance schematic map
You should bypass the obstacles to reach the goal.
end
Collision!!

## Slide 5: Score
 | Simulation (70%) | Real world (30%)
Automatic tracking | 35% | 12%
Parking | 15% | 9%
Avoidance | 20% | 9%

## Slide 6: Simulation Environment

## Slide 7: JetBot Simulator
Message
Server
Physical Simulator
Wrapper
Camera View
Control Signal
Link: https://reurl.cc/z8EK3e (for windows)

## Slide 8: Message Server
Dataserver.exe
  Run Server
  Run Unity3D Simulator
  Run Python Client
  Run Server
  Run Unity3D Simulator
  Run Python Client

## Slide 9: Unity3D Simulator
Camera on the jetbot
Map Selection
Simulator
Camera Switch
Debug Control
Set Motor Value
Take a photo (save at Unity-Simulator/Snapshot/)

## Slide 10: Obstacles

## Slide 11: Camera Switch
Free Camera: The camera can be controlled by mouse.
3rd Person Camera: The camera is above behind the vehicle.
Top Camera: The camera is above the vehicle and captures the top view with orthogonal projection.
Free Camera
3rd Person Camera
Top Camera

## Slide 12: Python Wrapper
jetbotSim
  Camera
    Wait for the camera data published by Unity3D simulator and invoke the callback function.
  Robot
    Send JSON-format control message to Unity3D simulator.
Note: The websocket library is required
pip install websocket
pip install websocket-client

## Slide 13: Example
from jetbotSim import Robot, Camera
import cv2
frames = 0
def execute(change):
global robot, frames
print("\rFrames", frames, end="")
frames += 1
# Control Example
if frames == 1:
robot.forward(0.2)
if frames == 80:
robot.left(0.05)
# Visualize
img = cv2.resize(change["new"],(640,360))
cv2.imshow("camera", img)
robot = Robot()
camera = Camera()
camera.observe(execute)

## Slide 14: Control API
robot.set_left_motor(value)
  Left_motor = value
robot.set_right_motor(value)
  Right_motor = value
robot.set_motor(value_l, value_r)
  Left_motor = value_l
  Right_motor = value_r
robot.add_motor(value_l, value_r)
  Left_motor += value_l
  Right_motor += value_r
Note:
The unit of motor value shown on Unity3D simulator (deg/sec) is different from the unit of control value in python wrapper (m/sec).

## Slide 15: Control API
robot.forward(value)
  Left_motor = value
  Right_motor = value
robot.backward(value)
  Left_motor = -value
  Right_motor = -value
robot.left(value)
  Left_motor = -value
  Right_motor = value
robot.right(value)
  Left_motor = value
  Right_motor = -value

## Slide 16: Control API
robot.stop()
  Left_motor = 0
  Right_motor = 0
robot.reset()
  Left_motor = 0
  Right_motor = 0
  Set to origin

## Slide 17: Hint
You can apply image processing and simple rule-base algorithm to detect the center of road and utilize P-control to track the road.
Detect
Horizon
Road
Center
P-gain

## Slide 18: Demo

## Slide 19: Real World Demo

## Slide 20: Real world score – 30 points
 | Test map | Real map
Automatic tracking | 4 points | 8 points
Parking | 3 points | 6 points
Avoidance | 3 points | 6 points
 | You can only restart at the origin | You can restart at the previous position 3 times

## Slide 21: Demo Process
The demo process contains two parts (for both test and final map).
  First part
    Automatic tracking & Parking
  Second part
    Automatic tracking & Parking & Avoidance

## Slide 22: Example - first

## Slide 23: Example - second

## Slide 24: Real world score – Details
 | Test map | Real map
Automatic tracking | Tracking red line: 4 points | Tracking red line: 8 points
Parking | Basic line: 1 point Perfect line: 3 points | Basic line: 2 points Perfect line: 6 points
Avoidance | 1 obstacle: 3 points (A little collision is ok) | 6 obstacles: 1 point/obstacle (A little collision is ok)
 | You can only restart at the origin | You can restart at the previous position 3 times

## Slide 25: Demo date
7/1:
  13:00~13:40
  14:00~14:40
  15:00~15:40
  16:00~16:40
7/2:
  8:00~8:40
  9:00~9:40
  10:00~10:40
  11:00~11:40
  13:00~13:40
  14:00~14:40
Please contact the TAs if you cannot demo in these timeslots or have any problems.

## Slide 26: Data directory
Everyone can share the collected data via TEAMS.

## Slide 27: Hint 1 - memory usage
sudo -H pip3 install jetson-stats
sudo jtop
memory

## Slide 28: Hint 2 - reference code
JupyterLab
http://<jetbot_ip_address>:8888

## Slide 29: Hint 3 - others
Recommend model: lightweight model, ex: shufflenet, mobilenet
Do not update pytorch
If your jetbot have any problem, you can restart the jetbot first!!!
  (Ex: camera dead)